### IDOC exchange monitoring
#### Purpose
This monitor is dedicated to the monitoring of IDOC messages. It will look for ERROR or WAITING status of messages received with a given period of time. You can customize the monitoring by creating specific rules depending on the client, the message type, the partner and the direction.
#### Configuration hints
Use the surveillance table to adjust the monitoring settings: Thresholds, severity, filters, etc...
Note: The time period must be configured in a consistent way together with the schedule time of the monitor: If the monitor is configured to run every 15 minutes, it is advised to set a period of 15 minutes too. You can set longer periods if you want to catch the number of errors within a large time frame, for statistics purpose.
With a period of 10 minutes, when the monitor runs at 12:00, it will look for IDOC messages occurred between 11:50 and 12:00.
#### Surveillance table
Parameter	Description
Active	Use this field to activate or deactivate a line of configuration.
Client	A filter to match only IDOC messages for/from a given client
Message type	A filter to match only IDOC message of a given type
Partner	A filter to match only IDOC for/from a given partner
Status code	A filter to match only IDOC in error state with a particular status code
Direction	Defines the direction of the IDOC messages to look for
Status	Define the type of status to look for.
Time period (min)	Defines how far in the past the monitor will look for IDOC messages at each check.
Max error	The threshold for the maximum number of IDOC messages matching the filters and status settings.
Aggregate	If enabled, the monitor will count the number of IDOC matching the filter and send an alarm if it reaches the threshold. If not enable, it will send an alarm per IDOC.
Severity	The severity of the alarm.
Auto clear	If checked, the alarm will be cleared as soon as the alarm condition is not met anymore.
Alarm tag	This field allows to add custom text within the alarm message. %MSG% variable will contain the actual generated message and can be used such as: “my_prefix %MSG% my_suffix”. By default, tag will be used as prefix.
Alarm	If checked, this line of surveillance will be used for alarm generation.
Metric	If checked, this line of surveillance will be used for metric generation.
Report	If checked, this line of surveillance will be used for report generation.

#### Examples
Active	Client	Message type	Partner	Status code	Direction	Status	Time period (min)	Max error	Aggregate	Severity	Auto clear	Alarm tag	Alarm	Metric	Report
true	*	*	*	*	ANY	ERROR	15	1	TRUE	MAJOR	true		true	false	false

Effect : Sends a MAJOR alarm if an IDOC message with an ERROR status is found in the last 15 minutes
#### Examples
Active	Client	Message type	Partner	Status code	Direction	Status	Time period (min)	Max error	Aggregate	Severity	Auto clear	Alarm tag	Alarm	Metric	Report
true	800	*	*	*	INBOUND	WAITING	60	10	TRUE	WARNING	true		true	false	false

Effect : Sends a WARNING alarm if 10 or more IDOC messages with WAITING status from client 800 are found in the last 60 minutes.
#### Generated metrics
metricId	metricUnit	metricTarget	metricDescription
FAILED_IDOC_MESSAGES	IDOCS	[CLIENT][DIRECTION][TYPE][PARTNER][ERROR_CODE]	Sends the number of failed IDOCS matching the filter. Target field will be set according to how specific is the configuration
WAITING_IDOC_MESSAGES	IDOCS	[CLIENT][DIRECTION][TYPE][PARTNER][ERROR_CODE]	Sends the number of waiting IDOCS matching the filter. Target field will be set according to how specific is the configuration