### HANA replication status
#### Purpose
System replication in HANA is a key component to be resilient against hardware failures or data corruption. This monitor will check that the replication system is in the expected state, during its nominal and transition phases (init,sync). It will also check for reconnects and fail overs and notifies as soon as those situations are detected.
#### Configuration hints
To start monitoring replication, create a new rule in the surveillance table. You can filter on the host and port number of the instance to customize the monitoring for specific nodes.
Expected mode: Define the expected mode of the replication, sends alarm if different
Error severity: Check for the replication status as visible in the system and send an alarm if in error
Fully recoverable: Check for the fully recoverable status as visible in the system and send an alarm if not as expected
Max init/sync/unknown time Check for the time spent in the corresponding state and send an alarm if the replication systems stays in that state for too long.
Reconnect/Failover count Check for reconnect or fail over situations. If the delta between now and last check is over threshold, send an alarm.
#### Surveillance table
Parameter	Description
Active	To enable/disable a rule.
Host	A filter on the host name of the instance
Port	A filter on the port number of the instance
Expected mode	Define the expected mode of the replication
Error Severity	If not DISABLED, send an alarm if the replication status is in error.
Fully recoverable Severity	if not DISABLED, send an alarm if the fully recoverable state is not true.
Max init time	The maximum time spent in init state
Max sync time	The maximum time spent in sync state
Max UNKNOWN time	The maximum time spent in unknown state
Max reconnect count	The maximum reconnects occurred since last check
Max failover count	The maximum failovers occurred since last check
Auto clear	If checked, the alarm will be cleared as soon as the alarm condition is not met anymore.
Alarm tag	This field allows to add custom text within the alarm message. %MSG% variable will containthe actual generated message and can be used such as: “my_prefix %MSG% my_suffix”. By default, tagwill be used as prefix.
enable Alarm	To enable alarm sending
enable QOS	To enable metric sending

#### Generated metrics
metricId	metricUnit	metricTarget	metricDescription
REPLICATION_STATUS	Boolean	SITE/HOST/PORT	Send TRUE if the replication status is OK, FALSE instead
REPLICATION_IS_SECONDARY_ACTIVE	Boolean	SITE/HOST/PORT
REPLICATION_IS_SECONDARY_FULLY_RECOVERABLE	Boolean	SITE/HOST/PORT	Send TRUE if the fully recoverable status is TRUE, FALSE instead
REPLICATION_RECONNECT_COUNT	Reconnects	SITE/HOST/PORT	Sends the number of reconnects since last check
REPLICATION_FAILOVER_COUNT	Failovers	SITE/HOST/PORT	Sends the number of failovers since last check