### SAP buffers
#### Purpose
This monitor will look for SAP buffers used space, hit ratio, directory used, swap rate and quality. Hit ratio, swap rate and buffer quality metrics can be computed since the startup of the instance, or within a period of time.
#### Configuration hints
Use the surveillance table to define the buffers monitoring settings: Buffer name, thresholds, severity, filters, etc... Note: Once you defined a surveillance line for a specific buffer name, other lines using “*” as buffer name filter will not match the specified buffer name. Multiple severity syntax: All thresholds can be defined by using the multiple severity syntax: - G2W:50 W2C:90 => Warning above 50, Critical above 90
If the period field is set with a value above 0, hit ratio, swap rate and buffer quality will be computed within the specified period instead of since the startup of the instance
#### Atomic fields
Low footprint (if false the swap/quality and min request rates will be computed)	With this option selected, the probe will use a low footprint API to get SAP buffers information from SAP. The drawback is that it won't be possible to compute the swap/quality rate and the number of requests.

#### Surveillance table
Parameter	Description
Active	Use this field to activate or deactivate a line of configuration.
Instance	A filter to match only a subset of instances.
Buffer name	The name of the buffer to look for, or * for any buffer.
Max used space (%)	The threshold for the current used space of a given buffer (percent).
Min hit ratio (%)	The threshold for the minimum hit ratio for a given buffer. Computed from instance startup or within a period.
Max dir used (%)	The threshold for the maximum swap rate of a given buffer. Computed from instance startup or within a period.
Max swap (%)	The threshold for the minimum quality rate of a given buffer. Computed from instance startup or within a period.
Min quality (%)	The threshold for the maximum directory usage of a given buffer. Computed from instance startup or within a period.
Period (min)	If a value greater than 0 is set, it will define the period for the computation of hit ratio, swap and quality rate metrics. Computed since startup otherwise.
Min requests	Define a minimum of requests to consider the computed metrics as relevant. Below this value, no alarms will be sent.
Severity	The default level of severity of the alarm generated by this line of surveillance. Applies when multiple severity syntax is not used
Auto clear	If checked, the alarm will be cleared as soon as the alarm condition is not met anymore.
Alarm tag	This field allows to add custom text within the alarm message. %MSG% variable will contain the actual generated message and can be used such as: “my_prefix %MSG% my_suffix”. By default, tag will be used as prefix.
Alarm	If checked, this line of surveillance will be used for alarm generation.
Metric	If checked, this line of surveillance will be used for QOS generation.
Report	If checked, this line of surveillance will used for showing threshold and severity in the daily report

#### Examples
Active	Instance	Buffer name	Max used space (%)	Min hit ratio (%)	Max dir used (%)	Max swap (%)	Min quality (%)	Period (min)	Min requests	Severity	Auto clear	Alarm tag	Alarm	Metric	Report
true	*	*	80%	90%					200	MAJOR	true		true	false	false

Effect : Sends a MAJOR alarm if any buffer use more than 80% of its space of if the hit ratio is below 90%.
#### Examples
Active	Instance	Buffer name	Max used space (%)	Min hit ratio (%)	Max dir used (%)	Max swap (%)	Min quality (%)	Period (min)	Min requests	Severity	Auto clear	Alarm tag	Alarm	Metric	Report
true	*	Program		90%		10%		30	200	MAJOR	true		true	false	false

Effect : Sends a MAJOR alarm if the Program buffer hit ratio of the last 30 min is below 90%, and if the swap rate of the period is over 10%
#### Generated metrics
metricId	metricUnit	metricTarget	metricDescription
BUFFER_PERCENTAGE USED	Percent	[INSTANCE][BUFFER]	The usage ratio of the buffer
BUFFER_USED_SPACE	Kilobytes	[INSTANCE][BUFFER]	The space used in the buffer
BUFFER_DIRECTORY_USED	Percent	[INSTANCE][BUFFER]	The directory used space of the buffer
BUFFER_HIT_RATIO	Percent	[INSTANCE][BUFFER]	The buffer hit ratio
BUFFER_SWAP_RATE	Percent	[INSTANCE][BUFFER]	The buffer swap rate
BUFFER_QUALITY	Percent	[INSTANCE][BUFFER]	The buffer quality rate