## MSSQL connector
### Purpose
- With the MSSQL connector, you can connect to an MSSQL database via a JDBC driver.
- The database will then be monitored by querying information from the database with SQL requests
- To create connector, there are two steps:
  - Create a user profile in the database and register it in Redpeaks
  - Create and set connector parameters
### Create user profile
- User profiles can be created via the Configure menu
- Once created, the user profile can be selected in the connector form
- Note: A user profile is by default associated with a company . You can explicitly set a profile to be cross companies. The effect is that it will be selectable from connectors of any companies.
- The corresponding user must be created in the database as well.
### Create connector
- Select the system in the Systems tree and select “Add connector” in its contextual menu, choose MSSQL type.
- Fill in the connector parameters:
  - Title The display name of the connector
  - Host: The hostname or IP address of the database host
  - Port: The port of the database service
  - Database name: The database to connect to
  - User: The user profile to use for the connection
  - Properties: Optional properties to add to the connection parameters (separated with semicolon (;)
Press Save & Test to save the profile and check the connection is working

### SSH
- In case you must connect to a database through an SSH tunnel, you can enable the SSH option and fill the parameters:
  - Host: The host where the entrance of the tunnel is created.
  - Port: The local port of the SSH tunnel
  - User: The user to authenticate on the SSH end point.
### Custom timeout
See Custom timeouts

### Authorizations
- Read access to below tables must be granted:
  - msdb.dbo.backupset
  - sys.master_files
  - sys.database_files
  - sys.dm_os_performance_counters
  - sys.configurations
  - sys.dm_os_volume_stats
  - sys.dm_io_virtual_file_stats