# Alerts
This monitor will collect the current alerts from HANA statistics engine.
## Configuration hints
- By default, this monitor will generate an alarm for each collected HANA alert matching the minimum severity settings, set to LOW by default.
- Use the configuration table to create specific monitoring rules such as:
  - Exclude a particular host
  - Implement specific severity mapping
  - Manage specific alert id.
### Default severity Mapping
HANA alert	Generated severity
ERROR	CRITICAL
HIGH	MAJOR
MEDIUM	MINOR
LOW	WARNING
INFORMATIONAL	INFORMATIONAL

## Configuration
### Atomic fields
Auto clear	If checked the alarms will be cleared if the alert is not present anymore in the statistics engine
Minimum severity	The minimum severity of the alerts
Send metadata	When active, this will send collected alerts as metadata to redpeaks cockpit

### Configuration table table
Parameter	Description
Active	If checked, the rule is enabled and will be evaluated
Host	Filters alerts associated to this specified host
Alert id	Filters on a specific alert id
Min rating	Filters on the rating of the alert. Only alerts with a rating higher or equal to the specified rating will be processed
Rating mapping	Use this field combined with Severity mapping. Select the alert rating to associate with the severity of the generated alarm
Severity mapping	The severity to associate with the selected rating
Auto clear	If active, the generated alarms will be cleared automatically when the corresponding HANA alert will be cleared
Use index	If active, the index of the HANA alert will be used in generated alarm id, making it unique
Alarm tag	Sets an arbitrary tag for alarms generated by this rule. It can then be used for filtering in alarm rules