# Elasticsearch Plugin
## Purpose
- This plugin allows you to send alarms, metric and monitor metadata directly to an Elasticsearch instance
- Alarms, metrics and monitor metadata can be indexed in separate Elasticsearch indices
- Built-in retry mechanism on Elasticsearch overload (HTTP 429 / rejected execution)
- Supports bulk indexing, buffering to protect Elasticsearch under load
## Configuration
- From the plugin menu of Redpeaks, select Elasticsearch in the plugin drop-down and press Add.
- The plugin has the following parameters:
Parameter	Description	Mandatory
Active	Enables or disables the Elasticsearch plugin	Yes
Configuration	Choose between Standard Configuration or Cloud Configuration	Yes
Hostname	The IP address or hostname of the Elasticsearch instance (Standard Config)	Yes
Port	The port used to connect to Elasticsearch (Default is 9200)	Yes
Cloud ID	The Cloud ID used for connecting to a cloud-based Elasticsearch instance (Cloud Config)	Yes
API Key	The API key for authentication (Cloud Config)	Yes
Name	A unique name for the plugin instance	Yes
Alarm Index	The Elasticsearch index where alarms will be stored	Yes (if Send alarms checked)
Metric Index	The Elasticsearch index where metrics will be stored	Yes (if Send metrics checked)
Metadata Index	The Elasticsearch index where metadata will be stored	Yes (if Send metadata checked)
Username	The username for Elasticsearch authentication	No
Password	The password for Elasticsearch authentication	No
Properties	A semicolon-separated list of additional Elasticsearch properties	No
Max queue size	The maximum size of the queue holding alarms and metrics	Yes
Send alarms	If active, alarms received by the plugin will be sent to Elasticsearch	No
Send metrics	If active, metrics received by the plugin will be sent to Elasticsearch	No
Send Metadata	If active, metadata received by the plugin will be sent to Elasticsearch	No
Split Metadata	Sends metadata as multiple documents (one per array element)	No
Use Datastream	Uses datastream templates and datastream indexing (recommended for time-series)	No
Create Templates	Automatically creates index templates (required for datastream mode)	No
Use Compression	Enables HTTP compression on Elasticsearch requests	No

### Indices
You can configure different indices (or prefixes) for alarms, metrics, and metadata.
- When Create Templates is enabled, the plugin automatically creates index templates
- When Use Datastream is enabled, data is indexed into Elasticsearch datastreams
If templates are disabled and datastream too, the plugin can attempt a fallback index creation if an index does not exist
### Properties
- Properties are key/value pairs separated by semicolon: setting1=value1;setting2=value2
- Common Elasticsearch properties include settings for index refresh intervals, number of replicas, etc.
## Example
### Standard Configuration

### Cloud Configuration

Note: Ensure that the Elasticsearch instance is reachable and properly configured to accept data from Redpeaks The configured user or API key must have permission to write documents and manage templates if enabled
## Troubleshooting
If you encounter issues:
- Verify the hostname and port (Standard Configuration) or the Cloud ID and API key (Cloud Configuration)
- Check Elasticsearch logs for any errors related to authentication or index operations
- Ensure that the indices specified in the configuration exist in Elasticsearch and have the appropriate permissions set for the configured user
- If Elasticsearch is overloaded (HTTP 429), consider reducing the batch size or increasing cluster capacity